VHF Booklet

Imagine what may happen if a distress situation were to take place and you or a guest on your boat needed to place some form of priority call.  In the excitement of the moment, it is easy to forget the proper procedure.  It would be handy to have a reminder of what buttons to press on your radio and the form of the different types of calls.

This program uses WORD.  You modify this document required and then print this out.  It becomes a small-sized booklet that can fit into a handy space near your radio.  Advise guests that in the event that they need to make a priority call, information relating to your radio will be found there.

After printing out the booklet, you should laminate the pages with a simple kit available at office supply stores.  This will waterproof the booklet.  This is especially needed if you use an ink-jet printer because most ink-jet printouts will run if they get wet.

If you have a DSC radio, the exact sequence of buttons to press can vary from model to model.  Refer to your User’s Guide and modify the instructions to match your equipment.

The instructions in green are for standard VHF radios, the instructions in orange are for DSC radios.  Before printing, delete the sections that do not apply to your equipment.

Before modifying the text, copy the file ‘Booklet.doc’ from the CD to your hard drive, then use WORD to work on the document.  Be careful to keep the information on each page in the same location where it is so that the tabs will match up with the data (e.g., Distress information will be found when you select the Distress tab).

Where it says ‘Capri’ in the sample text, you will change ‘Capri’ to the name of your vessel before printing the booklet.  In that way, the booklet becomes customized to match your vessel.  Where there is a description of the vessel, you will substitute the proper description of your boat.

Print using ‘Page Layout Printing’.  In Word, with some printers this is accomplished by choosing “File”, “Print”, “Properties”, “Page Setup” and select “Page Layout Printing” under “Printer Type”.  The settings depend on the options available on your model of printer.

You can create tabs by trimming with a scissors along the line on the right edge of the pages.  These tabs will make it easier to find the correct page.

Starting on page 1 (after the cover) there is also a trim line along the left edge of each page.  Cut all pages that have a trim line on the left side.

Discard these first two instruction pages and begin your booklet with the following sheet which is the cover.

With some printers, you may have to adjust the margins.

This document is intended to be printed two pages per sheet of paper.  By cutting along the lines, you end up with a compact booklet with two rows of tabs.

Trim

along

these

lines

on

the

rest

of

these

pages

DISTRESS CALL

For both standard AND DSC 	radios, select Channel 16.

For a DSC radio. . .

Input the vessel’s position (latitude and

longitude and UTC time (if the radio is not

connected to a GPS or a LORAN).  To do

this. . .

- Push DSC/ENT twice

- Rotate channel selector to set a digit

- Push CH/WX to advance the cursor or SCAN to move cursor backwards

- Push HI/LO to clear data

- Push DSC/ENT after you have set your position

- Set time then press DSC/ENT

To set distress type,

- push DSC/ENT,

- select DSC menu

- use channel selector choose ‘DTRS set’

- press DSC/ENT and select type (flooding,

collision, etc.)

- Press DSC/ENT

To make the Distress call. . .

Lift Distress button cover, hold down button

for five seconds.  When acknowledgement is

received, the system switches to channel 16.

Page 1

# Making a Mayday (Distress call) on a

# standard radio.

Select Channel 16

# MAYDAY, MAYDAY, MAYDAY

# This is (Capri, Capri, Capri)

MAYDAY, Capri

# Position is (state your location)

Vessel is a 32 foot Bayliner cruiser, white with

green trim

4 persons on board

Type of Distress (sinking, fire, explosion etc.)

# Plan of Action (abandoning ship, advise if there

# is a dinghy, if people are wearing life jackets)

This is Capri

Over

Page 2

MAYDAY RELAY CALL

Select Channel 16

(There is no digital Mayday relay call, 	only

a regular voice call on Channel 16).

# MAYDAY RELAY, MAYDAY RELAY, 	MAYDAY RELAY

This is Capri, Capri, Capri

MAYDAY (the name of the distress vessel)

Location of the Distress vessel

Nature of the distress (sinking, personal 	injury, etc.)

Number of persons on board

Their plan of action

Capri

# Over

Page 3

CANCELLATION OF DISTRESS

Cancellation of distress is done by voice only.

Select Channel 16

MAYDAY

# ALL STATIONS, ALL STATIONS,

# ALL STATIONS

This is Capri

Time (filing time of message, spelt

phonetically,

e.g., one eight three zero Eastern Standard)

Name of vessel in distress

# SEELONCE FEENEE

# Reason why Distress situation is being 	 cancelled (e.g.  all persons safe on board

# Your vessel. Distressed vessel has sunk)

Capri OUT

Establish contact with the Coast Guard and 	make certain they know that the distress

has been cancelled.

Page 4

URGENCY CALL

For both standard AND DSC 	radios, select Channel 16.

For DSC radios

  - push DSC/ENT,

  - select DSC menu

  - use channel selector choose ‘All Ships’

  - press DSC/ENT

  - press DSC/ENT again to make the call

Select Channel 16

For standard radios. . .

# PAN PAN, PAN PAN, PAN PAN

ALL STATIONS, ALL STATIONS,

ALL STATIONS

(Or if addressed to a specific station, transmit

that name three times)

This is Capri, Capri, Capri

# Position is (your location)

Vessel is a 32 foot Bayliner cruiser, white with                     	green trim

The urgency situation (damaged rudder, 	unable to steer, out of gas,. . . )

Request (need tow)

Capri  OVER

Page 5

CANCELLATION OF URGENCY

Select Channel 16 (there is no DSC

cancellation, it must be done manually)

Pan Pan

All Stations, All Stations, All Stations

This is Capri, Capri, Capri

(Give reason for cancellation such as ‘Under 	tow to Marina’)

Urgency Ended

Capri Out

Page 6

SAFETY CALL

For DSC radios, select Channel 06

  - push DSC/ENT,

  - select DSC menu

  - use channel selector choose ‘All Ships’

  - press DSC/ENT

  - press DSC/ENT again to make the call

Both standard and DSC radios. . .

Select Channel 16

SECURITE, SECURITE, SECURITE,

ALL STATIONS, ALL STATIONS,

ALL STATIONS

This is Capri, Capri, Capri

# Safety message concerning ……… to follow on         	channel - (06)

# PAN PAN

# ALL STATIONS, ALL STATIONS,

# ALL STATIONS

This is Capri, Capri, Capri

Give reason for cancellation (e.g., under tow to marina)

# URGENCY ENDED

Capri  OUT

Switch to Channel 06 and pass on the safety             	message as follows on the next page.

Page 7

# SECURITE, SECURITE, SECURITE

ALL STATIONS, ALL STATIONS, ALL STATIONS

This is Capri, Capri, Capri

Safety message (e.g., large deadhead floating near…

menace to navigation)

# Capri

# OUT

Page 8

Routine Calls (call an individual

station)

For DSC radios, select the channel you will be

communicating on.

Push DSC/ENT

Use the channel selector, choose ‘Individual’

and push DSC/ENT.

Use channel selector to choose an MMSI# or

select ‘Manual set’.

Press DSC/ENT to transmit call.

Standby for acknowledgement.  When one

is received, system changes to the channel you

selected.

Calling on a standard (non-DSC) radio.

Select calling frequency (usually Channel 16)

(Name of friend’s boat, repeated three times)

This is Capri, Capri, Capri

Over

After making contact, switch to a working

channel.

Page 9

Phonetic Alphabet

Alpha

Bravo

Charlie

Delta

Echo

Foxtrot

Golf

Hotel

India

Juliett

Kilo

Lima

Mike

November

Oscar

Papa

Quebec

Romeo

Sierra

Tango

Uniform

Victor

Whiskey

X-Ray

Yankee

Zulu

Page 10